## Slide 1
INDUSTRIAL ML · IoT & SENSORS
IoT-based Predictive Maintenance
for Industrial Motors
Real-time motor failure risk prediction from live sensor telemetry, using a Random Forest classifier trained on the AI4I 2020 Predictive Maintenance dataset.
ML + ECE Capstone Project
Combined Machine Learning & Electronics/Communication Engineering
Jaziya Shaheen K A
Punniya K Siju
INTEL Lab Training Batch
July 2026

## Slide 2
Problem Statement
Why predictive maintenance matters for rotating industrial equipment
The Challenge
Unplanned motor failures halt production lines, causing costly downtime and emergency repairs.
Traditional maintenance is either reactive (fix after failure) or purely time-based (fixed schedules) — both waste resources.
Rotating machinery emits measurable signals — temperature, torque, rotational speed, tool wear — before failure occurs.
Goal: build an ML model that reads live sensor readings and predicts failure risk in real time, enabling condition-based maintenance.
5
Live sensor inputs used for prediction
AI4I
2020
Public benchmark dataset (10,000 records)
Binary +
Prob.
Failure flag & calibrated risk probability

## Slide 3
System Architecture
End-to-end pipeline: sensors → preprocessing → model → live dashboard
Sensor Input
Product type, air/process temp, rotational speed, torque, tool wear
→
Preprocessing
Cleaning, scaling & encoding of live/historical telemetry
→
Random Forest
Model
Trained classifier estimates failure probability
→
Web Dashboard
Streamlit-style UI shows live risk assessment
Deployment: the trained model is served behind a live web form (predictive-core.lovable.app) — operators enter current readings and instantly get a failure prediction plus probability score, no code required.

## Slide 4
Dataset & Feature Engineering
AI4I 2020 Predictive Maintenance Dataset — synthetic, physically realistic motor telemetry
Product Type
Quality tier (Low / Medium / High) — encoded categorical feature
Air & Process Temp.
290–310K / 300–320K — thermal stress indicators
Rotational Speed
1000–3000 rpm — mechanical load signal
Torque
0–80 Nm — driving-force / strain measurement
Tool Wear
0–260 min — cumulative wear/degradation proxy
Feature Scaling
Numerical features normalized; categorical one-hot/label encoded

## Slide 5
ML Model Selection
Random Forest classifier — chosen for tabular sensor data with mixed feature types
Why Random Forest?
Handles mixed categorical + numerical sensor features without heavy preprocessing
Robust to noise and outliers common in live telemetry
Ensemble of decision trees reduces overfitting vs. a single tree
Outputs both a class label and a calibrated probability — ideal for risk scoring
Feature importance gives interpretable insight into which sensor drives risk
Training Pipeline
1
Train/Test Split
Stratified split preserving rare failure-class ratio
2
Hyperparameter Tuning
Grid/Random search over n_estimators, max_depth, min_samples_leaf
3
Class Imbalance Handling
Class weighting to address rare failure events
4
Cross-Validation
K-fold CV to validate generalization before deployment
5
Model Export
Serialized model integrated into the live prediction API

## Slide 6
Performance Metrics
Evaluation approach for the failure-prediction classifier (fill in final measured values)
Chart: Illustrative Target Metrics
| Accuracy | Precision | Recall | F1-Score | ROC-AUC
Score (%) | 96 | 88 | 82 | 85 | 94
Note: values shown are illustrative placeholders — replace with the actual metrics from your trained model's test set.
Confusion Matrix (concept)
TN
FP
FN
TP
Priority: minimize False Negatives (missed failures) — a missed failure is costlier than a false alarm.
Also report: ROC curve, precision-recall curve, and feature importance ranking to explain which sensors drive risk.

## Slide 7
Working Demo — Live Dashboard
predictive-core.lovable.app — real-time inference from live sensor input
predictive-core.lovable.app
Predictive Maintenance Dashboard
Live Prediction — enter current sensor values to estimate failure risk
Product Type
Air Temperature (K)
Process Temperature (K)
Rotational Speed (rpm)
Torque (Nm)
Tool Wear (min)
Predict Failure Risk
What the Dashboard Does
Accepts 5 live sensor readings + product quality tier as input
Feeds values into the trained Random Forest model in real time
Returns a binary failure prediction (Yes/No)
Displays a calibrated failure probability score for risk-based scheduling
Built to let operators act before a breakdown occurs — no code needed

## Slide 8
Key Challenges
Obstacles encountered across data, modeling, and deployment
Class Imbalance
Failure events are rare in the AI4I dataset, risking a model biased toward predicting 'no failure'. Addressed via class weighting and careful metric choice (recall over raw accuracy).
Feature Relevance
Not all raw sensor signals contribute equally; determining which combination of temperature, torque, speed, and wear best predicts failure required iterative feature analysis.
Sim-to-Real Gap
AI4I is synthetic-but-realistic; a live dashboard must handle sensor noise and out-of-range values gracefully, unlike a clean offline dataset.
Real-Time Deployment
Packaging a trained scikit-learn model behind a responsive live web form (predictive-core.lovable.app) that returns predictions instantly for arbitrary user input.
Overfitting vs. Generalization
Tuning Random Forest depth/estimators to fit training patterns without memorizing noise, validated via cross-validation.
ECE-ML Integration
Bridging domain knowledge of motor telemetry (ECE) with correct ML preprocessing/evaluation practice — the core ask of this capstone.

## Slide 9
Deliverables & Conclusion
What's complete, what's documented, and what's next
Jupyter Notebook
Preprocessing, EDA, feature engineering, RF training & tuning, evaluation
GitHub Repository
Structured repo with code, dataset link, professional README
Slide Deck
This presentation — problem, architecture, model, metrics, challenges
Working Demo
Live dashboard at predictive-core.lovable.app for real-time inference
Next Steps
Finalize hyperparameter tuning and report final Accuracy / Precision / Recall / F1 / ROC-AUC on held-out test data
Add feature-importance visualization to the dashboard for interpretability
Stress-test the live form with edge-case and out-of-range sensor values
Complete GitHub README with setup instructions and dataset download guide